## Slide 1: Efficient Soft Error Protection for Commodity Embedded Microprocessors using Profile Information
Daya S Khudia, Griffin Wright and Scott Mahlke
Computer Science and Engineering
University of Michigan
Ann Arbor

## Slide 2: Soft Errors
Soft errors, also called single-event upsets(SEUs)
  Occur because of
    Neutrons from cosmic rays
    Alpha particles from packaging materials
    Voltage fluctuations or signal interference
Parameters affecting soft error rates
  Technology scaling
  Voltage scaling
Image credit: Certichip
Notes: A critical aspect of any computer system is reliability. One pervasive cause of computer system failure and the focus of this work is soft errors. A soft error or SEU can be induced by high energy particle strike from cosmic radiation and chip packaging material or by electrical noise. Unlike manufacturing or design defects, which are persistent, transient faults as their name suggests, only sporadically influence program execution.
Soft Errors: As the industry moves towards finer process geometries, however the soft error rate may drastically increase.

## Slide 3: Soft error rate (SER)
Past
Present
Future
Aggressive voltage scaling
(near-threshold computing)
One failure per MONTH per 100 chips
One failure per DAY per 100 chips
One failure per DAY per chip
[Feng’10, Shivakumar’02]
At high error rates, mainstream systems can experience unacceptable soft errors
  There is a need for mainstream solutions
Notes: 1 FIT means that the mean time before an error occurs is a billion device hours.
IBM targets 114 FITs. Which would require a mean time before an SEU causes an undetected error of roughly 1000 years.

## Slide 4: Traditional Architectural Solutions
Traditional dual/triple – modular redundancy
  Run on separate hardware and compare results
  Mission-critical reliability w/ high hardware costs
[IBM Z-series, HP NonStop]
Utilize multiple threads (temporal) instead of separate hardware (spatial)
  Retain high coverage but sacrifice performance costs to save area
[AR-SMT, Reunion]
Perform selective checking
  software invariants
  critical μarch structures
[ARGUS, DIVA, Reddy:DSN`08]
Redundant execution in a single-threaded context
  compiler interleaves original and redundant instructions
  “tunable” coverage
[SWIFT, EDDI]
Relies on anomalous behavior to identify faults
  extremely cheap
  decent coverage
[RESTORE, SWAT]
Bridge the gap between symptom-based schemes and instruction duplication
  “reliability for the masses”
  sacrifice a little on coverage to maintain very low costs
Increasing Fault Coverage
Increasing Overheads (area, power, performance, etc.)
n-Modular Redundancy
Redundant Multi-threading
Invariant Checking
Symptom-based
Shoestring
Instruction Duplication
Performance Overhead
and
Fault Coverage Target
Notes: `Spatial or temporal redundant execution has long been a cornerstone for detecting soft errors,
with hardware DMR (dual-modular redundancy) and TMR (triplemodular redundancy) being the solutions of choice for missioncritical systems.
The basic idea was to use the processor’s extra SMT contexts to run two copies of the same thread, a leading
thread and a trailing thread. The leading thread places its results in a buffer, and the trailing thread veriﬁes these results and commits the executed instructions.
DIVA is less expansive alternative to full duplication utilizing a small checker core to monitor computations performed by a larger core.
Reddy: Simple checks on uarch structures to ensure they are working correctly.

## Slide 5: Proposed Solution
Target solution
Fault coverage from different sources of masking (75% to 92%)
Increasing Overheads (performance)
Instruction duplication-based detection
Symptom-based detection
Hardware exceptions
Branch mispredicts
Cache misses
Target solution
Increasing Fault Coverage
  Provide affordable reliability for commodity systems on
  a cheap budget
      Exploit cheap symptom-based fault detection
      Judiciously apply sw-level instruction duplication to improve coverage

## Slide 6: Contributions
Exploit synergy between symptoms and SW-duplication
A software solution to generate intelligent code to detect soft errors
  No user annotations are required
Profile based intelligence in the analysis
  Memory profiling and Edge profiling
    Some instructions are more important than others
  Value profiling for generating more software symptoms
    Exploit statistical invariance

## Slide 7: Outline
Background
System level overview
Intelligent duplication
Profiling techniques
Experimental evaluation
Conclusions

## Slide 8: System Overview
Intelligent Duplication
Instrument and get profile data for
  edge-profiling
  memory profiling for alias analysis
  value profiling
Profiling
Analyze program structure
Load profile data and perform selective duplication
Operating System
Physical Hardware
Trigger Lightweight recovery based on
  selective symptoms (hardware exceptions)
  comparison fail in duplicated code
Runtime
Compilation
Notes: One such solution is safetynet.

## Slide 9: Compilation
Code analysis and intelligent duplication
  can be used with code written in various languages
  Is independent of target machine
For our Low-cost solution, we target an ARM backend
intermediate representation (IR)
Code analysis and intelligent duplication (IR to IR)
Code generation
Application source code
Application binary
analyses and optimizations
Classification
Analysis
Duplication

## Slide 10: Baseline Classification and Analysis
High value instructions:
  Likely to produce corrupted program output if they consume corrupted input
Symptom-generating instructions:
  Likely to produce symptom if they consume corrupted inputs
Safe Instructions:
  Normally covered by symptom generating instructions
Refs: Shoestring, EDDI , SWIFT
ld1
call printf (---, op1, ---)
op1 = ld1 + 1
op1
ld1 = load addr
---
addr = addr1 + 8
Safe
Symp-Gen
High Value
Notes: EDDI => 2002
SWIFT => 2005

## Slide 11: Instruction Duplication
Recursively duplicate instructions starting from operands of high-value instructions
  Stop if
    Already duplicated
    Safe
    No more producers
==
Recovery or continue execution
original instrs
duplicated
cmps and branches
Safe
Symptom generating
High value
---
---

## Slide 12: Baseline Coverage and Overhead
90% of fault coverage at 40.50% overhead
Chart: Fault coverage breakdown
| 164.gzip | 181.mcf | 186.crafty | 254.gap | 255.vortex | 256.bzip2 | Average
Benchmarks | 0 | 0 | 0 | 0 | 0 | 0 | 0
Fault Coverage | 95 | 66 | 80 | 82 | 82 | 65 | 470
SWDetect | 3 | 11 | 10 | 3 | 8 | 9 | 44
Symptoms | 1 | 1 | 4 | 7 | 3 | 12 | 28
Silent corruptions | 1 | 22 | 6 | 8 | 7 | 14 | 58
% Overhead | 52.08 | 44.74 | 32.59 | 31.75 | 39.05 | 42.51 | 40.78
Goal: Reduce overhead without affecting fault coverage

## Slide 13: Profile Based Duplication
Memory Profiling
  Silent stores
    Need not be protected because expected to write the same value again
  Get load/store alias information
Edge Profiling
  Do not protect an infrequently executed instruction by duplicating frequently executing instructions
Value Profiling
  Use the statistical invariance to generate more software symptoms
By incorporating dynamic behavior, perform intelligent duplication

## Slide 14: Refined Duplication Process
ld1
call printf (---, op1, ---)
op1 = ld1 + 1
op1
ld1 = load addr
Store dt1, addr
st1
dt1 = incr + 1
Dop1
Dop1 = ld1 + 1
cmp
Dst1
Dst1 = Dincr + 1
cmp
Trigger recovery
---
---
br
original instrs
duplicated
cmps and branches
Trigger recovery
br
F
T
F
T
---
Control flow
Data flow
Dependence through memory
lib calls
Only consider lib calls
Notes: Consider lib calls
Dependence through memory
Memory is protected by other means

## Slide 15: Memory Profiling: Silent Stores
A store is silent if it writes the already existing value at memory location
A large fraction of silent stores exist and can be exploited for intelligent code duplication
Chart: % of silent stores (dynamic)
| 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parser | 253.perlbmk | 254.gap | 255.vortex | 256.bzip2 | average
% Dynamic silent stores | 8.19 | 18.2447 | 73.3543 | 50.44 | 16.48 | 18.1162 | 51.3441 | 14.73 | 57.95 | 1.59 | 31.0439

## Slide 16: Exploiting Silent Stores
ld1
call printf (---, op1, ---)
op1 = ld1 + 1
op1
ld1 = load addr
store dt1, addr
st1
dt1 = incr + 1
Dop1
Dop1 = ld1 + 1
cmp
Dst1
Dst1 = Dincr + 1
cmp
Trigger recovery
---
---
br
original instrs
duplicated
cmps and branches
Trigger recovery
br
F
T
F
T
---
Silent stores are expected to write the same value again soon
silent store
Control flow
Data flow
Notes: As long as the last store is not wrong, this optimization wouldn’t cause any harm.

## Slide 17: Edge Profiling: Recursive Duplication Break
Do not protect a non frequently executed instruction by duplicating a frequently executed instruction
BB0:
BB1:
BB2:
20
2000
Control flow
Data flow
BB3:
BB4:
10
10

## Slide 18: Value Profiling
What are the most frequently value produced by an instruction?
If a value is produced more than 99% of the times, use that value for symptom generation
add
xor
Most of the times, result is 0
Most of the times, result is 71

## Slide 19: Creating Software Symptoms
If in a chain of instruction, last instruction produces the same value
  Insert the comparison with the frequently generated value
---
op
---
Generates the same value very frequently

## Slide 20: Software Symptom Generation
---
op2
call printf (---, op1, ---)
op1 = op2 + 1
op1
---
op2 = op3 * op4
Dop1
Dop1 = Dop2 + 1
cmp
Dop2 = Dop3 * Dop4
cmp
Trigger recovery
br
original instrs
duplicated
cmps and branches
Trigger recovery
br
F
T
F
---
0
Dop2
---
---
T
Produces 0 more than 99%
Notes: More efficient to check for symptoms.

## Slide 21: Evaluation Methodology
Program analysis, Profiling and intelligent duplication
  Implemented as compiler pass in the LLVM compiler
Input sensitivity of profiling
  train input of SPECINT2K for training
  ref input for the actual fault injection runs
Statistical fault injection (SFI) experiments
  GEM5 simulator in ARM syscall emulation mode
Random (single) bit flip in physical register file
  Simulated entire benchmarks after fault injection
  Log files analyzed for results classification
Notes: Symptoms
Silent stores profiling implemented as an extension of Loop Aware Memory Profiling (LAMP)
Value Profiling implemented as instrumentation pass in LLVM
are unusual behavior. With value profiling, we are providing a mechanism for generating symptoms.

## Slide 22: Fault Injection Outcome Classification
Masked
  No corruption in the program output
SWDetects
  Detected by duplication
Covered by symptoms
  Produces a symptom such as page fault in 1000 cycles of fault injection
Failures
  Fail status on program termination or program did not terminate in 20 Hrs.
SDCs (Silent Data Corruptions)
  Fault injections which results in user visible corruptions
Notes: SDC are the most catastrophic types of error and will affect the system’s data integrity

## Slide 23: Performance Overhead
Chart: % Overhead
| 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parser | 253.perlbmk | 254.gap | 255.vortex | 256.bzip2 | average
Full duplication | 65.81 | 51.497 | 40.4114 | 60.29 | 59.66 | 39.9314 | 45.3311 | 37.63 | 42.49 | 62.08 | 50.5131
Profile oblivious duplication | 52.08 | 31.227 | 24.1544 | 44.74 | 32.59 | 19.6248 | 31.1733 | 31.75 | 39.05 | 42.51 | 34.89
Profile aware duplication | 33.92 | 28.9587 | 19.1975 | 13.96 | 27.54 | 15.5305 | 24.9699 | 10.67 | 16.89 | 13.93 | 20.5567
  Over 40% reduction in overhead

## Slide 24: Fault Coverage
Chart: Fault Coverage
| full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | full-dup | pro-oblivi | pro-aware | 164.gzip | 175.vpr | 176.gcc | 181.mcf | 186.crafty | 197.parser | 253.perl | 254.gap | 255.vortex | 256.bzip2 | average
Masked | 98 | 60 | 78 | 65 | 61 | 64 | 79 | 83 | 74 | 40 | 702
SWDetects | 2 | 23 | 12 | 27 | 30 | 17 | 12 | 6 | 13 | 40 | 182
Symptoms | 0 | 13 | 7 | 0 | 0 | 12 | 4 | 0 | 1 | 1 | 38
Failures | 0 | 1 | 3 | 5 | 5 | 5 | 2 | 8 | 8 | 14 | 51
SDCs | 0 | 3 | 0 | 3 | 4 | 2 | 3 | 3 | 4 | 5 | 27
pro-oblivi Masked | 95 | 66 | 85 | 66 | 80 | 71 | 80 | 82 | 82 | 65 | 772
pro-oblivi SWDetects | 3 | 23 | 7 | 11 | 10 | 10 | 9 | 3 | 8 | 9 | 93
pro-oblivi Symptoms | 0 | 8 | 5 | 0 | 0 | 12 | 4 | 1 | 1 | 0 | 31
pro-oblivi Failures | 1 | 1 | 2 | 9 | 7 | 5 | 2 | 13 | 3 | 21 | 64
pro-oblivi SDCs | 1 | 2 | 1 | 14 | 3 | 2 | 5 | 1 | 6 | 5 | 40
pro-aware Masked | 95 | 74 | 78 | 65 | 77 | 75 | 84 | 84 | 85 | 68 | 785
pro-aware SWDetect | 3 | 19 | 7 | 3 | 12 | 10 | 5 | 1 | 3 | 15 | 78

## Slide 25: Conclusions
Proposed software-only low overhead fault detection technique
  yields intelligent and efficiently duplicated code
Profile based analysis
  Silent stores need not be protected
  Don’t protect infrequently executed instructions by duplicating frequently executed instructions
  Value profiling can be used to generate software symptoms
Intelligent duplication yields
  Over 40% reduction in overhead
  Statistical insignificant difference in fault coverage

## Slide 26
Thank You! Questions?