## Slide 1: Low-Power Scientific Computing
Ganesh Dasika,
Ankit Sethia, Trevor Mudge, Scott Mahlke
University of Michigan
Advanced Computer Architecture Laboratory
NDCA 2009

## Slide 2: The Advent of the GPGPU
Growing popularity for scientific computing
  Medical Imaging
  Astrophysics
  Weather Prediction
  EDA
  Financial instrument pricing
Commodity item
Increasingly programmable
  Fermi
  ARM/Mali ?
  “Larrabee” ?

## Slide 3: Disadvantages of GPGPUs
Gap between computation and bandwidth
  933 GFLOPS : 142 GB/s bandwidth
  (0.15B of data per FLOP, ~26:1 Compute:Mem Ratio)
Very high power consumption
  Graphics-specific hardware
  Several thread contexts
  Large register files and memories
  Fully general datapath
Inefficiencies in all
general-purpose architectures

## Slide 4: Goals
Architecture for improved power efficiency for high-performance scientific applications
  Reduced data center power
  Improved portability for mobile devices
  100s of GFLOPS for 10-20W
GPU-like structure to exploit SIMD
Domain-specific add-ons
System design for best memory/performance balancing

## Slide 5: Performance vs. Compute Power
Pentium M
Core 2
IBM Cell
Core i7
GTX 280
GTX 295
S1070
Cortex
A8

## Slide 6: High Throughput at Low Power
Medical domains
  Image reconstruction
Communications, signal-processing
  Real-time FFT for GPS receivers
  Parity-checking for WiMAX and WiFi
Financial applications
  Fluctuation analysis for various market indices
  SDE or Monte Carlo-based pricing models

## Slide 7: Application Analysis
Chart: 
| acfdtd2d | sde | volatility | mbir
FPU | 7 | 43 | 18 | 7
SFU | 0 | 10 | 1 | 0
Mem | 8 | 20 | 7 | 4
AGU | 8 | 3 | 4 | 3
CF | 5 | 5 | 5 | 3
I-ALU | 0 | 14 | 0 | 0
Primarily FP computation
Significant mem usage
(approx 0.9B/instr)
Some complex AG

## Slide 8: Performance vs. Computer Power vs. Bandwidth
Pentium M
Core 2
IBM Cell
Core i7
GTX 280
GTX 295
S1070
GTX 280
GTX 295
Bandwidth limited!!
~0.15 B/instr vs
~0.9 B/instr
Cortex
A8

## Slide 9: eco-GPGPU
FP MAC pipeline
Shuffle-swizzle networks
Co-processors for math functions
Significantly less power than Nvidia GPUs

## Slide 10: Current Architecture
500 MHz @ 65 nm
64-way SIMD
64 GFLOPs
~2.5 W/core
1 TFLOP
@ 16 cores, 40 W

## Slide 11: Performance vs. Compute Power
Pentium M
Core 2
IBM Cell
Core i7
GTX 280
GTX 295
S1070
Cortex
A8
eco-GPGPU

## Slide 12: Memory System?
Multiple eco-GPGPU will eventually hit memory wall
GPGPUs use 1,000s of thread contexts to hide latency
  Too much area
  Too much power

## Slide 13: Options for Memory System
3D-stacked DRAM?
  Increased B/W
  Reduced latency
  Multi-threading not necessary
Caches?
  32-64KB required assuming 200-cycle DRAM latency
  Helps when temporal locality required
Pre-fetching, streaming?
  Most data accesses are streaming/stride-based
  Addresses predictable
Compression?
  Sparse-matrix data easily compressible
  Somewhat application-specific

## Slide 14: Speedup from Streaming
Chart: 
| acfdtd2d | sde | volatility | mbir | average
 | 0.28571 | 0.031579 | 0.11429 | 0.17647 | 0.15201

## Slide 15: Options for Memory System
3D-stacked DRAM?
  Increased B/W
  Reduced latency
  Multi-threading not necessary
Caches?
  32-64KB required assuming 200-cycle DRAM latency
  Helps when temporal locality required
Pre-fetching, streaming?
  Most data accesses are streaming/stride-based
  Addresses predictable
Compression?
  Sparse-matrix data easily compressible
  Somewhat application-specific

## Slide 16: Data Compression in Medical Imaging
Normally for reducing disk space
Use compression to reduce data transfer instead
~10:1 loss-less compression
Re-reconstructed
after 12:1 JPEG lossy compression
of sinogram

## Slide 17: JPEG-LS Compression Hardware
Low area footprint, compared to FPUs
  ~0.25mm2
High throughput
  ~250 Mpixels/sec
Very low power dissipation
  ~2mW
Compressing more data => Better ratios
  [De]Compress data at off-chip mem bus
10X more bandwidth
Chart: 
| 512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
 | 11.2562 | 10.3745 | 9.4736 | 8.4387 | 7.5807 | 5.1985 | 3.869 | 2.8061 | 1.6902 | 1.3048
Compression Ratio
Image rows per compression
vs

## Slide 18: Current/Future Work
Thorough analysis of scientific compute domains
  % FP
  Mem:Compute ratios
  Data access patterns
Improved GPU measurements
  CUDA profiler to determine performance
  Power measurements
Memory system options

## Slide 19: Conclusions
Low-power “supercomputing” an important direction of study in computer architecture
Current solutions either over-designed or far too inefficient
Significant efficiency improvements:
  Datapath optimizations
  Reduce thread contexts
  Improved memory systems

## Slide 20: Thank you!
???