## Slide 1: A Bypass First Policy for Energy-Efficient Last Level Caches
Jason Jong Kyu Park1, Yongjun Park2, and Scott Mahlke1
1University of Michigan, Ann Arbor
2Hongik University

## Slide 2: Last Level Cache (LLC)
Large portion of the chip area
  About 20% in i7-5960X (Cores ≈ 30%)
Has large impacts on:
  Performance
  Energy consumption
[Intel Core i7-5960X]

## Slide 3: Trends in LLC
Increasing in size
Chart: Year
| 2010.5 | 2011.25 | 2012.75 | 2013.8 | 2014.8 | 2015.8
Apple | 0.5 | 1 | 1 | 4 | 4 | 4
Intel | 8 | 15 | 20 | 25

## Slide 4: LLC Characteristic
Large number of never-rereferenced blocks
  Bypasses: RRIP [Jaleel’10], PDP [Duong’12], DSB [Gao’10]
Chart: Never-rereferenced
| sphinx3 | bzip2 | wrf | hmmer | mcf | astar | cactusADM | avg-all | mpeg4dec | jpg2000dec | avg-all | SPEC | Mediabench
OPT | 0.59843 | 0.78686 | 0.76603 | 0.6175 | 0.95209 | 0.80611 | 0.93359 | 0.76388 | 0.25151 | 0.756 | 0.45299
RRIP | 0.91664 | 0.66323 | 0.88211 | 0.8016 | 0.91905 | 0.85857 | 0.922 | 0.89458 | 0.85007 | 0.81284 | 0.77526
PDP | 0.27018 | 0.54077 | 0.84953 | 0.54347 | 0.88139 | 0.6413 | 0.67357 | 0.80504 | 0.47531 | 0.81476 | 0.61395
DSB | 0.52407 | 0.69326 | 0.93266 | 0.88532 | 0.99268 | 0.98783 | 0.98734 | 0.90465 | 0.754 | 0.79238 | 0.66603
Still large number of never-rereferenced blocks!

## Slide 5: Cache First Policy
Common traits
  Inserts into the LLC before identifying characteristics
  Conservative in decisions
LLC
Upper Level Caches
Unnecessary writes of never-rereferenced blocks!

## Slide 6: Objective of This Work
Design of a Bypass First Policy (BFP)
  Defaults to bypassing
    Removes unnecessary writes of never-rereferenced blocks
    Energy saving
Design Challenges
  How do we know when to insert?
  Can we implement BFP such that it also improves performance?

## Slide 7: Locality in the LLC
Many cache blocks are reused in the upper level
  BFP will handle majority of cache blocks
Chart: Reused Blocks
| sphinx3 | bzip2 | wrf | hmmer | mcf | astar | cactusADM | avg-all | mpeg4dec | jpg2000dec | avg-all | SPEC | Mediabench
OPT | 0.40157 | 0.21314 | 0.23397 | 0.3825 | 0.047908 | 0.19389 | 0.066412 | 0.23612 | 0.74849 | 0.244 | 0.54701

## Slide 8: Observation 1: Temporal Locality
When a block is reused,
  The same block is likely to be reused
Chart: Cache Hit Distribution
| sphinx3 | bzip2 | wrf | hmmer | mcf | astar | cactusADM | avg-all | mpeg4dec | jpg2000dec | avg-all | SPEC | Mediabench
Single Reuse | 0.091382 | 0.0035106 | 0.19648 | 0.013601 | 0.017438 | 0.29998 | 0.0055785 | 0.1594 | 0.44428 | 0.002933 | 0.21385
Multiple Reuses | 0.90862 | 0.99649 | 0.80352 | 0.9864 | 0.98256 | 0.70002 | 0.99442 | 0.8406 | 0.55572 | 0.99707 | 0.78615

## Slide 9: Observation 2: Spatial Locality
When a block is reused,
  Blocks within the same memory region are likely to be reused
Chart: Misses between hits in 128kB memory region
Locality exists once a reuse has been observed!

## Slide 10: BFP Overview
Set 0
LLC
Set 1
Set 2
…
Set N
Shadow Directory
…
Width
Valid
Tag
Spatial Locality Predictor (SLP)
…
Depth
Valid
Tag
Confidence

## Slide 11: BFP Design: Insert Decision
LLC
Hit
Miss
Shadow Directory
Bypassed blocks store tags in shadow directory or SLP
Hit
Spatial Locality Predictor (SLP)
…
…
Insert!
Miss
Hit
Miss
Bypass!

## Slide 12: BFP Design: Management
Shadow Directory
Spatial Locality Predictor (SLP)
…
…
Bypassed Block
Round-robin replacement
Hit

## Slide 13: Determining Parameters
Experimentally sweep to find the parameters
  e.g.) Number of bits for tag
Chart: Tag bits
| 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
 | 0.36591 | 0.28014 | 0.207 | 0.13013 | 0.055633 | 0.020789 | 0.002643 | 0.0026348 | 0.0017771 | 0.0017081 | 0.0017073 | 0.0014378 | 0.0014378

## Slide 14: BFP and Inclusion Property
Bypass breaks inclusion property
  Bypass buffer [Gupta’13]
LLC
Bypass buffer
Energy consumption
LLC >>> Bypass buffer

## Slide 15: Experimental Setup
CMP$im
  A pin-based trace-driven simulator
    Desktop-class CPU for SPEC2006
      4-way out-of-order, 128-entry ROB, three-level caches
    Mobile CPU for Mediabench
      4-way out-of-order, 128-entry ROB, two-level caches
  Baseline: LRU
CACTI
  Models power for cache structures
  22nm technology LSTP (Low Standby Power) process

## Slide 16: Energy Saving
Chart: Energy Reduction (%)
| sphinx3 | bzip2 | wrf | hmmer | mcf | astar | cactusADM | avg-all | mpeg4dec | jpg2000dec | avg-all | SPEC | Mediabench
RRIP | 0.29349 | 0.096449 | 0.013654 | 0.42415 | 0.091659 | 0.11694 | 0.16183 | 0.053943 | 0.078537 | 0.016597 | 0.0026185
PDP | 0.64831 | 0.043321 | 0.26546 | 0.7549 | 0.070673 | 0.79238 | 0.70029 | 0.4111 | 0.040817 | 0.0746 | 0.054847
DSB | 0.66947 | 0.14015 | -0.0020058 | 0.66815 | 0.49694 | 0.28184 | 0.49645 | 0.41052 | 0.0032065 | 0.085703 | 0.022159
BFP | 0.66249 | 0.20226 | 0.035221 | 0.78187 | 0.67589 | 0.82862 | 0.78184 | 0.57129 | 0.42916 | 0.1263 | 0.21651
41.1%
41.1%
5.4%
57.1%

## Slide 17: Performance Comparison
Chart: IPC Improvement (%)
| sphinx3 | bzip2 | wrf | hmmer | mcf | astar | cactusADM | gmean-all | mpeg4dec | jpg2000dec | gmean-all | SPEC | Mediabench
RRIP | 0.58646 | 0.031634 | 0.022858 | 0.1262 | 0.28828 | 0.088349 | 0.37037 | 0.047822 | -0.017678 | 0.050616 | -0.0012295
PDP | 0.67435 | -0.0017673 | 0.054831 | 0.21206 | 0.00293 | 0.068785 | 0.25838 | 0.050147 | 0.010812 | 0.0052962 | -0.0044334
DSB | 0.65814 | 0.030378 | -0.0002277 | 0.19698 | 0.3561 | 0.10219 | 0.44154 | 0.058427 | -0.0060771 | 0.06026 | 0.014646
BFP | 0.66527 | 0.045215 | 0.0054241 | 0.17331 | 0.34182 | 0.097724 | 0.43029 | 0.056586 | -0.0080173 | 0.055862 | 0.012824
5.8%
4.0%
4.8%
5.7%

## Slide 18: Hardware Overhead
 | RRIP | PDP* | DSB | BFP
Per line | 2 bit | 2 bit | 5 bit | 1 bit
Per set |  |  | 22 bit | 31 bit
Per sampled set |  | 515 bit | 748 bit | 
Extra | 10 bit | 10K gates 0.13kB | 51 bit | 27 bit
Total | 8.0kB | 10.14kB + 10K gates | 31.3kB | 11.75kB
*PDP requires logic to compute PD, which is 10K gates

## Slide 19: Summary
Bypass First Policy vs. Cache First Policy
  A large number of never-rereferenced blocks even for the optimal replacement
BFP
  Apply temporal locality and spatial locality when a reuse has been observed
    Shadow directory
    Spatial locality predictor
  57.1% energy saving for entire SPEC2006
  5.7% performance improvement for entire SPEC2006

## Slide 20: Questions