## Slide 1: ELF: Maximizing Memory-level Parallelism for GPUs with Coordinated Warp and Fetch Scheduling
Jason Jong Kyu Park1, Yongjun Park2, and Scott Mahlke1
1University of Michigan, Ann Arbor
2Hongik University

## Slide 2: GPUs in Modern Computer Systems
Chart: Year
| 2001.583 | 2003.83 | 2004.5 | 2004.58 | 2005.58 | 2006.5 | 2006.834 | 2007.0 | 2008.5 | 2009.0 | 2009.917 | 2010.33 | 2010.834 | 2011.58 | 2011.917 | 2012.334 | 2012.417 | 2013.16 | 2013.5 | 2013.834 | 2014.75 | 2014.88
CPU | 3.2 | 5.6 | 24 | 85.44 | 96 | 102.4 | 158.4 | 224 | 224 | 448 | 896
GPU | 19.47 | 54 | 165 | 518 | 933.12 | 1345 | 1581.056 | 3090.432 | 4499.712 | 5046 | 5600

## Slide 3: GPU Usage
Latency-critical
  Frame rate
Throughput-oriented
  Resource utilization

## Slide 4: Reality: Achieved Performance
GTX480
  Achieves 40% of peak performance
Chart: Achieved Performance
| BFS | BP | BS | BT | CP | FDTD | HIST | HS | HW | KM | LBM | LC | LMD | LPS | LUD | MRIQ | MUM | NW | PF | RS | SGEMM | SRAD | ST | SpMV | TPACF | average
 | 0.137 | 0.71275 | 0.5898 | 0.33198 | 0.56496 | 0.38353 | 0.29376 | 0.54797 | 0.61872 | 0.39783 | 0.12083 | 0.30673 | 0.12482 | 0.70359 | 0.21482 | 0.53446 | 0.092744 | 0.13995 | 0.1744 | 0.43985 | 0.7935 | 0.19868 | 0.70603 | 0.24095 | 0.8553 | 0.409

## Slide 5: GPU Execution Model
Inside streaming multiprocessor (SM)
Fetch
Issue
Warp:
Issue
: Warp scheduler

## Slide 6: GPU Execution Model
Issue
Commonly used warp scheduling
Fetch
Issue
RR (Round robin)
GTO (Greedy then oldest)

## Slide 7: Exposed Memory Latency
Assuming Maxwell architecture
~300 cycles for memory latency
Upto 2 instruction issues per cycle
16 warps per warp scheduler (4 warp schedulers)
…
  # of instructions per warp to hide memory latency
    300 / 15 * 2 ≈ 40

## Slide 8: Stall Reasons
Chart: Cycles (%)
| BFS | BP | BS | BT | CP | FDTD | HIST | HS | HW | KM | LBM | LC | LMD | LPS | LUD | MRIQ | MUM | NW | PF | RS | SGEMM | SRAD | ST | SpMV | TPACF | average
Memory Dependency | 0.17627 | 0.092962 | 0.3878 | 0.32215 | 0.0097613 | 0.3707 | 0.3434 | 0.074419 | 0.10516 | 0.28503 | 0.056927 | 0.0095815 | 0.098576 | 0.20449 | 0.13135 | 0.001592 | 0.13427 | 0.32151 | 0.24692 | 0.041062 | 0.17483 | 0.060052 | 0.07149 | 0.65739 | 0.0017 | 0.17518
Fetch | 0.0057211 | 0.0020525 | 0.0025695 | 0.050664 | 0.022467 | 0.16799 | 0.070846 | 0.0083709 | 0.031039 | 0.0084333 | 0.044341 | 0.40269 | 0.011624 | 0.012195 | 0.30163 | 0.044107 | 0.025534 | 0.077024 | 0.13709 | 0.033312 | 0.00053358 | 0.0075115 | 0.0010068 | 0.025965 | 0.0020523 | 0.059871
Memory Conflict | 0.6795 | 0.052078 | 0.0067723 | 0.28023 | 0.11105 | 0.027237 | 0.27842 | 0.24738 | 0.16884 | 0.29316 | 0.71249 | 0.017471 | 0.717 | 0.049586 | 0.18097 | 0.068161 | 0.74505 | 0.34307 | 0.35514 | 0.44836 | 0.0080377 | 0.72035 | 0.21424 | 0.064157 | 0.0015014 | 0.27161
Others | 0.0015091 | 0.14016 | 0.013048 | 0.014983 | 0.29176 | 0.050536 | 0.013565 | 0.12186 | 0.07624 | 0.015545 | 0.06541 | 0.26353 | 0.047977 | 0.030138 | 0.17122 | 0.35168 | 0.0024008 | 0.11844 | 0.086453 | 0.037413 | 0.023093 | 0.013412 | 0.0072332 | 0.011543 | 0.13945 | 0.084344
8%
6%
18%
27%

## Slide 9: Objective of This Work
Maximize Memory-level Parallelism
Fetch
Issue
Issue
L1I cache
LSU
Problem
- Memory Dependency Stalls
Solution
- Earliest Load First (ELF) scheduling
- Coordinated warp and fetch scheduling

## Slide 10: Objective of This Work
Maximize Memory-level Parallelism
Fetch
Issue
Issue
L1I cache
LSU
Problem
- Fetch Stalls
Solution
- Instruction prefetching

## Slide 11: Objective of This Work
Maximize Memory-level Parallelism
Fetch
Issue
Issue
L1I cache
LSU
Problem
- Memory Conflict Stalls
Solution
- Memory reordering

## Slide 12: Earliest Load First (ELF)
Overlap memory latency with other operations
: Compute
: Memory load
W0:
W1:
W2:
W3:
Next instructions
Schedule
: Memory latency
…
…
…
…
Lost issue slots
GTO
ELF

## Slide 13: Distance to Next Memory Load
Detected at compile time
8
2
Most of the time, distance is decreased by one
Distance may be recomputed after
  Memory load
  Branch
: Compute
: Branch
: Memory load
5
4

## Slide 14: Transferring Program Points
JIT compiler
  Embeds program points information in the binary
: Compute
: Branch
: Memory load
0
4
0
21
7
min
8
11
17

## Slide 15: Coordinated Warp and Fetch Scheduling
Use the same priority for issue and fetch
Fetch
Issue
Issue

## Slide 16: Instruction Prefetching
Prefetch instructions, but avoid memory contention
  If outstanding memory requests < ½ of maximum
Fetch
Issue
Issue
L1I cache
L1I cache miss

## Slide 17: Memory Reordering
: Stalled because of memory conflict
: Other requests
LSU
Re-execute later
Stall (MSHR full, associativity stall)
Allow other memory requests to go first
Hit-under-miss or no conflict

## Slide 18: Memory Reordering
: Load from Warp 0
: Load/Store from Warp N
: Store from Warp 0
: Stalled
: Stalled

## Slide 19: Experimental Setup
GPGPU-Sim v3.2.2
  GPU Model: GTX 480
    1536 threads per SM
    32768 registers per SM
    48kB shared memory per SM
Workloads
  25 benchmarks from NVIDIA SDK, Parboil, and Rodinia
  Baseline: Greedy-then-oldest (GTO) scheduler

## Slide 20: Performance Contribution
12%
4.1%
4.9%
2.5%
Chart: Performance Improvement (%)
| BFS | BP | BS | BT | CP | FDTD | HIST | HS | HW | KM | LBM | LC | LMD | LPS | LUD | MRIQ | MUM | NW | PF | RS | SGEMM | SRAD | ST | SpMV | TPACF | geomean
ELF: Scheduling | 0.0054067 | 0.0095745 | 0.00096679 | 0.023688 | 0.014439 | 0.03641 | 0.0095568 | 0.030343 | 0.014203 | 0.27658 | -4.3623e-05 | 0.010174 | 0.091847 | 0.13745 | 0.044266 | -0.00039493 | 0.05558 | 0.0090877 | 0.040341 | 0.15501 | 0.0053681 | -0.0008891 | 0.093634 | -7.5108e-05 | -0.00040354 | 0.040687
ELF: Instruction prefetch | 0.00079592 | 0.00069815 | 0.0084567 | 0.0008244 | 0.0076811 | 0.4942 | 0.028748 | 0.0014375 | -0.00050389 | 3.2293e-06 | -0.017386 | 0.78681 | -0.00086161 | 0.011351 | 0.11995 | 0.00070816 | -0.0064067 | 0.038722 | 0.0044631 | -0.00026047 | 0.0011728 | -0.0012584 | 0.011382 | 0.0018419 | 0.00026865 | 0.048569
ELF: Memory reordering | 0.069947 | 0.0010739 | -0.0057401 | 0.037052 | 0.017697 | 0.00081166 | 0.0082728 | 0.04036 | 0.018068 | 0.16462 | -0.040989 | 0.0046311 | 0.0083809 | -0.0039846 | 0.022261 | 0.0022446 | 0.045235 | 0.0021431 | 0.014902 | 0.034357 | -0.0022898 | 0.14432 | 0.069119 | 0.0052587 | -7.2116e-05 | 0.025382
ELF | 0.070353 | 0.0055003 | -0.012276 | 0.064188 | 0.030104 | 0.54362 | 0.051183 | 0.20631 | 0.055302 | 0.35062 | -0.057921 | 0.78887 | 0.10254 | 0.15548 | 0.16139 | 0.00070129 | 0.10681 | 0.04993 | 0.068581 | 0.20885 | 0.0091402 | 0.17317 | 0.17231 | -0.00045018 | -0.01626 | 0.11898
49%
79%
79%
54%

## Slide 21: Performance Comparison
2-LV | CCWS | DYNCTA | 
-3% | 1% | -2% | 
+ Good for cache-sensitive applications
- Not better than GTO in general
+ Tackles three types of stalls
+ Effective in general
ELF
12%

## Slide 22: Summary
Memory latency is still a problem in GPUs
  Compute vs. memory ratio ≈ 40 to hide the latency
ELF
  Maximize memory-level parallelism
    Earliest load first scheduling
      Coordinated warp and fetch Scheduling
    Instruction Prefetching
    Memory reordering
  12% performance improvement

## Slide 23: Questions