## Slide 1: WarpPool: Sharing Requests with Inter-Warp Coalescing for Throughput Processors
John Kloosterman, Jonathan Beaumont, Mick Wollman, Ankit Sethia, Ron Dreslinski, Trevor Mudge, Scott Mahlke
Computer Engineering Laboratory
University of Michigan

## Slide 2: Introduction
GPUs have high peak performance
For many benchmarks, memory throughput limits performance
Chart: % cycles stalled
| < 12% | 12-33% | 33-66% | 66%+
Frequency | 0.43956 | 0.18681 | 0.25275 | 0.12088

## Slide 3
32 threads grouped into SIMD warps
Warp scheduler sends ready warps to FUs
warp 0
1
2
47
warp scheduler
ALUs
Load/Store Unit
add r1, r2, r3
...
warp
thread
load [r1], r2
GPU Architecture

## Slide 4
Warp Scheduler
Intra-Warp Coalescer
Load/Store Unit
to L2, DRAM
Load
Group by cache line
Cache Lines
L1
MSHR
GPU Memory System
Notes: Walk through

## Slide 5: Problem: Divergence
Warp Scheduler
Intra-Warp Coalescer
Load/Store Unit
to L2, DRAM
Load
Group by cache line
Cache Lines
L1
MSHR
…
Notes: Problem statement here: “However, there are access patterns where this merging does not work.”
Super important to get across here: here, the bottleneck is not off-chip b/w or anything: it’s that ***we can’t get to the L1 cache to service anything, including hits***
-Need to set up that fixing the pipeline to the cache is something worth doing

## Slide 6
Warp Scheduler
Intra-Warp Coalescer
Load/Store Unit
to L2, DRAM
L1
MSHR
Problem: Bottleneck at L1
Warp 0
Warp 1
Warp 2
Warp 3
Warp 4
Warp 5
Loads
Group by cache line
Warp 0
Warp 1
Warp 2
Warp 3
Warp 4
Warp 5
Notes: In cases where there are loads waiting to be scheduled, we need to make every access to the cache count.
Example: scalar load

## Slide 7
Chart: 
| SYR2K | pf_1 | SYRK | mri-g_3 | spmv | sc | 3MM_1 | GEMM | 2MM_1 | CORR_3 | ATAX_1 | kmeans_2 | CORR_4 | MVT_1 | BICG_2 | GESUMMV | lbm | AVG
Cache lines per load/store | 12.83 | 12.61 | 10.86 | 8.46 | 3.52 | 1 | 1 | 1 | 1 | 1.98 | 32 | 17.16 | 11.99 | 11.33 | 11.32 | 8.77 | 1.22 | 8.7088
Waiting loads/stores | 13.26 | 2.7 | 16.31 | 3.31 | 3.82 | 22.86 | 12.01 | 8.93 | 8.77 | 4.94 | 2.51 | 15.59 | 2.78 | 3.44 | 3.77 | 3.95 | 4.71 | 7.8624
Hazards in Benchmarks
Memory Divergent
Bandwidth-Limited
Cache-Limited
Notes: Problem caused by too many requests
Can we merge requests?
Doubled cache sets or ways?
Big was 64x128x8
Small was 64x128x4
Doubled cache ways. Reason: hash algorithm

## Slide 8: Inter-Warp Spatial Locality
Spatial locality not just within a warp
warp 0
divergent inside a warp
warp 1
warp 2
warp 3
warp 4

## Slide 9: Inter-Warp Spatial Locality
Spatial locality not just within a warp
warp 0
warp 1
warp 2
warp 3
warp 4

## Slide 10: Inter-Warp Spatial Locality
Spatial locality not just within a warp
Key insight: use this locality to address throughput bottlenecks
warp 0
warp 1
warp 2
warp 3
warp 4

## Slide 11
1 cache line from
one warp
Inter-Warp Window
1 per cycle
1 per cycle, but on behalf of multiple loads: bandwidth
multiple per cycle: divergence
32 addresses
1 cache line from one warp
Warp
Scheduler
L1
Intra-Warp Coalescer
Intra-Warp Coalescer
Intra-Warp Coalescer
Inter-Warp
Coalescer
Warp
Scheduler
1 cache line from many warps
32 addresses
Intra-Warp Coalescer
many cache lines from many warps
L1
Inter-Warp Window
Notes: Make this similar to the problem slide with the bottlenecks?
Key things to get across:
-buffer requests in the inter-warp window: backpressure will be good!
-make intra-warp coalescer wider because we can service
Old vs. new comparison?

## Slide 12
Intra-Warp Coalescer
Intra-Warp Coalescer
Inter-Warp
Coalescer
Warp
Scheduler
Warp
Scheduler
L1
Intra-Warp
Coalescers
Inter-Warp
Queues
Selection Logic
L1
Design Overview
Notes: -Use matrix transpose example?

## Slide 13
Warp
Scheduler
...
Intra-Warp Coalescer
to inter-warp coalescer
Queue load instructions before address generation
Intra-warp coalescers same as baseline
1 request for 1 cache line exits per cycle
load
load
Address Generation
Queue memory instructions
Intra-Warp Coalescers
Notes: -Requests can stay in the intra-warp coalescers for multiple cycles.

## Slide 14
Many coalescing queues, small # tags each
Requests mapped to coalescing queues by address
Insertion: tag lookup, max 1 per cycle per queue
...
intra-warp
coalescers
sort by address
Cache line address
warp ID
thread mapping
...
...
Cache line address
warp ID
thread mapping
...
...
Inter-Warp Coalescer
W0
W0
Notes: How this works:
-the inter-warp queues have a request to issue each cycle
-there is a mapping of the address of that request to an inter-warp queue
-
Why many queues:
-

## Slide 15
Many coalescing queues, small # tags each
Requests mapped to coalescing queues by address
Insertion: tag lookup, max 1 per cycle per queue
...
intra-warp
coalescers
sort by address
Cache line address
warp ID
thread mapping
0
...
...
Cache line address
warp ID
thread mapping
...
...
Inter-Warp Coalescer
W0
W0
W0
Notes: How this works:
-the inter-warp queues have a request to issue each cycle
-there is a mapping of the address of that request to an inter-warp queue
-
Why many queues:
-

## Slide 16
Many coalescing queues, small # tags each
Requests mapped to coalescing queues by address
Insertion: tag lookup, max 1 per cycle per queue
...
intra-warp
coalescers
sort by address
Cache line address
warp ID
thread mapping
0
...
...
Cache line address
warp ID
thread mapping
0
...
...
Inter-Warp Coalescer
W1
W1
Notes: How this works:
-the inter-warp queues have a request to issue each cycle
-there is a mapping of the address of that request to an inter-warp queue
-
Why many queues:
-

## Slide 17
Many coalescing queues, small # tags each
Requests mapped to coalescing queues by address
Insertion: tag lookup, max 1 per cycle per queue
...
intra-warp
coalescers
sort by address
Cache line address
warp ID
thread mapping
0
1
Cache line address
warp ID
thread mapping
0
...
...
Inter-Warp Coalescer
Notes: How this works:
-the inter-warp queues have a request to issue each cycle
-there is a mapping of the address of that request to an inter-warp queue
-
Why many queues:
-

## Slide 18
Select a cache line from the inter-warp queues to send to L1
2 strategies:
  Default: pick oldest request
  Cache-sensitive: prioritize one warp
  Switch based on miss rate over quantum
...
L1
Cache
Selection Logic
Selection Logic
Notes: Question here: if inter-warp coalescing is good, why not do RR?
-Answer: because we have to maintain intra-warp temporal locality. Have done experiments with RR and also increasing latency in coalescer to get more coalesces. Tends not to be worth it: there’s a optimal point between priority and coalescing, and this design got close to it.

## Slide 19
Implemented in GPGPU-sim 3.2.2
  GTX480 baseline
  32 MSHRS
  32kB cache
  GTO scheduler
Verilog implementation for power and area
Benchmark criteria
  Parboil, PolyBench, Rodinia benchmark suites
  Memory throughput limited: waiting memory requests for more than 90% of execution time
WarpPool configuration
  2 intra-warp coalescers
  32 inter-warp queues
  100,000 cycle quantum for request selector
  Up to 4 inter-warp coalesces per L1 access
Methodology

## Slide 20
Chart: Speedup (x)
| SYR2K | pf_1 | SYRK | mri-g_3 | spmv | sc | 3MM_1 | GEMM | 2MM_1 | CORR_3 | ATAX_1 | kmeans_2 | CORR_4 | MVT_1 | BICG_2 | GESUMMV | lbm | GEOMEAN
8-way banked cache | 1.0295 | 0.93906 | 0.92662 | 1.0049 | 0.9957 | 1.0007 | 1.0172 | 1.0269 | 0.9979 | 1.0332 | 1.0215 | 1.0079 | 0.88235 | 0.95679 | 0.93696 | 0.95521 | 1.0208 | 0.98453
MRPB | 1.1856 | 0.88389 | 1.2229 | 0.98531 | 1.1603 | 2.3526 | 1.0543 | 1.0514 | 0.99013 | 0.93049 | 1.4595 | 1.7954 | 0.94185 | 1.333 | 1.3104 | 1.0376 | 1.0437 | 1.179
WarpPool | 1.8046 | 1.3248 | 2.0255 | 0.89841 | 1.0261 | 3.173 | 1.1014 | 1.0829 | 1.1032 | 0.9407 | 1.7342 | 5.1671 | 1.0029 | 1.1905 | 1.2171 | 0.96032 | 1.0854 | 1.3797
Memory Divergent
Bandwidth-Limited
Cache-Limited
3.17
2.35
5.16
Results: Speedup
1.38x
[1] MRPB: Memory request prioritization for massively parallel processors: HPCA 2014
Notes: 2 mechanisms: increased L1 throughput, decreased L1 misses
What to talk about this slidE:
-What the related work was
-Point out that banked cache didn’t see speedup
Have callouts for the bars we talk about
-This slide: highlight benchmarks for L1 thoughput, L1 misses mechanisms

## Slide 21
Chart: Requests Serviced per L1 access
| SYR2K | pf_1 | SYRK | mri-g_3 | spmv | sc | 3MM_1 | GEMM | 2MM_1 | CORR_3 | ATAX_1 | kmeans_2 | CORR_4 | MVT_1 | BICG_2 | GESUMMV | lbm | AVG
8-way banked cache | 1.05 | 1.31 | 1.63 | 1.02 | 1.47 | 1.05 | 1 | 1 | 1 | 1.36 | 1.29 | 1.14 | 1 | 1.39 | 1.38 | 1 | 1 | 1.1818
WarpPool | 1.338 | 1.0022 | 1.135 | 1 | 1.0366 | 1.285 | 1.2191 | 1.1979 | 1.2386 | 1.083 | 1.0002 | 1 | 1.0054 | 1.0019 | 1.0018 | 1.0015 | 1 | 1.091
Memory Divergent
Bandwidth-Limited
Cache-Limited
Results: L1 Throughput
Banked cache uses divergence, not locality
WarpPool merges even when not divergent
No speedup for banked cache: 1 miss/cycle
Notes: Key insights here:
-8 banks often better because doesn’t require matches with other warps
-B/W limited: the backup of instructions gives us more opportunity
But no speedup b/c only 1 miss/cycle, on behalf of one warp

## Slide 22
Chart: % Baseline MPKI
| SYR2K | pf_1 | SYRK | mri-g_3 | spmv | sc | 3MM_1 | GEMM | 2MM_1 | CORR_3 | ATAX_1 | kmeans_2 | CORR_4 | MVT_1 | BICG_2 | GESUMMV | lbm | GEOMEAN
MRPB | 0.82917 | 1.0535 | 0.7767 | 1.0154 | 0.83421 | 0.75243 | 0.84923 | 0.9141 | 0.90859 | 1.0154 | 0.76762 | 0.56912 | 0.99898 | 0.85143 | 0.85901 | 0.9975 | 0.99576 | 0.87239
WarpPool | 0.53413 | 0.9143 | 0.48048 | 1.004 | 0.93539 | 0.70729 | 0.86705 | 0.94645 | 0.89022 | 1.0333 | 0.72079 | 0.16152 | 0.98082 | 0.94044 | 0.91463 | 0.99548 | 0.99849 | 0.76894
Results: L1 Misses
Memory Divergent
Bandwidth-Limited
Cache-Limited
MRPB has larger queues
Oldest policy sometimes preserves cross-warp temporal locality
[1] MRPB: Memory request prioritization for massively parallel processors: HPCA 2014
Notes: The difference between our prioritization and MRPB:
We can reorder requests, not just load instructions
Kmeans_2: high level of divergence, we can interrupt a load that asks for 32 difference cache lines
When we do worse: because MRPB is bigger, because it doesn’t hold addresses

## Slide 23: Conclusion
Many kernels limited by memory throughput
Key insight: use inter-warp spatial locality to merge requests
WarpPool improves performance by 1.38x:
  Merging requests: increase L1 throughput by 8%
  Prioritizing requests: decrease L1 misses by 23%

## Slide 24: WarpPool: Sharing Requests with Inter-Warp Coalescing for Throughput Processors
John Kloosterman, Jonathan Beaumont, Mick Wollman, Ankit Sethia, Ron Dreslinski, Trevor Mudge, Scott Mahlke
Computer Engineering Laboratory
University of Michigan