## Slide 1
Bundled Execution of Recurring Traces for Energy-Efficient General Purpose Processing
Shantanu Gupta, Shuguang Feng, Amin Ansari,
Scott Mahlke, and David August
University of Michigan
(Intel, Northrup-Grumman, UIUC, Princeton)
MICRO-44 December 6, 2011

## Slide 2: Computational Efficiency Landscape
Pentium M
Core 2
Core i7
GTX 280
GTX 295
S1070
IBM Cell
AMD 6850
2
Embedded
Processors
AMD Opteron
Energy dilemma
  More gates can fit on a die
  But power constraints limit their use
  To scale performance, need to increase efficiency

## Slide 3: Where Does The Energy Go?
Energy used in a single-issue RISC in-order core
Instruction fetch and
decode energy dominates
Actual execution barely
consumes 10%
Plenty of opportunities to save energy….
[Dally’08]

## Slide 4: Increasing Efficiency with Accelerators
Accelerators can give 10 – 50X efficiency
FPGAs
General Purpose Processors
SIMD
Efficiency, Performance
Flexibility
Loop Accelerators,
ASICs
Application regularity defines success:
Small dominant code segments
Little control flow
Narrow application set
Data parallelism
ASIPs
DSPs
Notes: ASICs, accelerators, conservation cores, loop buffers…all these were used in embedded systems…
Regular codes is suitable…e.g. counted inner-most loops, modulo-schedulable codes, explicit data-parallelism, etc.
Small number of benchmarks…can use specialized hardware…

## Slide 5: Utility Factor for Accelerators
FPGAs
General Purpose Processors
SIMD
Efficiency, Performance
Flexibility
Loop Accelerators,
ASICs
ASIPs
DSPs
What fraction of the code gets accelerated?
Most solutions fail for “irregular” or “general-purpose” code
???
Goal: A design to target irregular codes
Notes: ASICs, accelerators, conservation cores, loop buffers…all these were used in embedded systems…
Regular codes is suitable…e.g. counted inner-most loops, modulo-schedulable codes, explicit data-parallelism, etc.
Small number of benchmarks…can use specialized hardware…

## Slide 6: The BERET Architecture
A compute engine for “hot regular regions” in irregular codes
Key insights:
  Exploits recurring instructions (traces) to save on redundant fetches and decodes
  Uses a bundled execution model to save on redundant register reads/writes
L1 D$
BERET
CPU
L1 I$
Program
Hot
Regions
CPU
BERET
copy live-ins
copy live-outs
BERET: Bundled Execution of REcurring Traces
Notes: Exclusive to every core. Everything else is according to our vision from the last year!
Works for irregular codes
Applied on recurring sequences of instructions (hot parts of a code)
Runs them using a subgraph execution model
Can be configured for any program segment

## Slide 7: Insight 1: Recurring Instructions
We leverage such looping traces for savings
Straight-line code  simple hardware
Typically short  easy to buffer
Significant fetch / decode savings for buffered instructions
How about loops?
  Typical loops in irregular codes are large and control intensive!
BB 1
BB 2
BB 5
BB 0
BB 20
BB 3
BB 4
BB 7
BB 6
85%
15%
90%
10%
50%
50%
Hot basic blocks
Control Flow
Graph (CFG)
BB 1
BB 2
BB 5
BB 3 exit?
BB 20
BB 4 exit?
A looping trace
BB 1
BB 2
BB 5
BB 20
Notes: Show CFG…hot trace..
Side branches trigger an exit to the original control-flow graph
Say that traces help us save redundant instruction fetches and decodes
Show trace coverage in some chosen benchmarks
Traces have been used in the past for dynamic code optimization…we exploit them to find temporal regularity in code sequences
Remember, these can have side exits…and the execution returns to the original Control flow graph

## Slide 8: Frequency of Recurring Instructions
Offload stable traces in irregular loops

## Slide 9: Insight 2: Bundled Execution
Traditional processors issue and execute instructions in isolation…
>>
ST
LD
+
/
>>
&
<<
ST
+
LD
>>
ST
LD
+
/
>>
&
<<
ST
+
LD
11 instrs, 14 reads, 10 writes
3 instrs, 6 reads, 2 writes
Bundled
execution
Notes: Subgraph-execution can save register accesses…
Can divide a data flow graph into constituent subgraphs…

## Slide 10: Efficiency of Bundled Execution
10
Chart: Bundle length
| 2 | 3 | 4 | 5
Perf/Power | 1.5452 | 1.8155 | 2.1866 | 2.5166
All results normalized to a bundle length of 1
Bundled execution increases datapath efficiency by more than 2x

## Slide 11: BERET Hardware Design
Hardware design objectives:
  Capable of executing straight-line code in a loop (traces)
  Support for bundled execution of trace instructions
  Handle trace side-exits, and transfer control to the main processor
Internal
Register File
SEB 1
SEB 2
SEB N
Writeback Bus
MUX
Store
Buffer
D$
ALU
LD
<<
ALU
Index bits
Input Latch
Output Latch
config. bits
Configure
SEB
1 – 2 cycles
Execute
SEB
1 – 5 cycles
Writeback
1 – 2 cycles
SEB
config.
Configuration RAM (CRAM)
I$
SEB: Subgraph Execution Block
Notes: This is a mini-processor, which is a microcoded CISC engine that can run only straight line code.
Configuration RAM stores the active program trace --- instruction fetch/decode savings..recurring trace storage
Each trace is broken down into bundles of instructions, executed on the SEBs. At a time, only one SEB is active --- SEB gives us bundled executioin…
Energy Savings also result from a simple hardware with a short pipeline, no control handling / speculation, smaller structures, fewer latches…

## Slide 12: Compiler Support
MPY
ADD
SUB
BR
LD
AND
SHIFT
ST
ADD
ADD
OR
BR
Hot Trace
exit
exit
SEB 0
SEB 1
SEB 2
SEB 3
Configuration
Control
RF
BERET with SEBs
Program
Hot Traces
(with high loop
back probability)
1
2
3
+
|
&
<<
ST
×
-
BR
LD
+
+
BR
1
2
3
Data flow
subgraphs
Assert
Assert
1. Trace Detection
2. Mapping traces to SEBs
Notes: These the flow of software support to map program regions to
Once mapped to BERET, run the sequence of SEBs back to back, until a trace exit is found. Control returns to the main processor in that case…

## Slide 13: CPU-BERET Execution Flow
CPU
BERET
RF
RF
Body
Header
…
Body
Header
Body
Header
Assert
Header
Side
Exit
Header
Copy Live-Ins
Copy Live-Outs
RF-0
RF-1
RF-0
RF-1
Execution Time
Execution
Registers copied to BERET
Program executes on BERET
Assert discovered, last iteration squashed
Registers copied back to main processor
Program executes on main processor

## Slide 14: Energy Savings
Training set
Test set
Notes: Chart 1: Energy consumption (normalized to full core) for the execution traces mapped to BERET hardware
Chart 2: Energy consumption for the entire program, parts of which run on BERET, and the rest runs on default core.
Energy savings against an ARM 1176 core : single-issue in-order
Performance comparison against the same design.
Training set is the set of workloads used to determine the collection of SEBs. The test set was a new set of benchmarks to measure the quality of identified SEBs.

## Slide 15: Performance Impact
Notes: Performance changes from running on the BERET engine. Overall, there is a 10% performance improvement. This speedup is a result of exploiting ILP in SEBs that execute instructions in parallel. This behavior is very similar to the subgraph level accelerators (CCA, Nate Clark et. al.).

## Slide 16: Concluding Remarks
Scaling program performance in energy-constrained environment requires improving computational efficiency
Most accelerators exploit program regularity for savings
BERET is a configurable engine that saves energy by:
  Exploiting hot traces to avoid redundant fetches and decodes
  Using a bundled execution model to reduce temporary variable reads and writes
Energy Saving
~35%
Performance Enhancement
~10%
Area Overhead
20%

## Slide 17: Questions
For more
  See http://cccp.eecs.umich.edu

## Slide 18: Fine Grain Program Phase Behavior
18
Traditional phases too coarse-grained to match accelerator
Traditional phases
Hypothesis of This Work
Irregular programs are composed of fine-grain periods of high degrees of regularity. We can identify these periods and run them on an accelerator customized for “simple” execution.
Accelerate the pink portions
0M
10M
Fine-grain